0. flash new firmware and new FPGA image
1. power cycle N200
2. remove all coax cables from N200
3. uhd_cal_rx_iq_balance
4. uhd_cal_tx_iq_balance
5. sudo uhd_cal_tx_dc_offset
6. repeat 3 to 5 two times

sudo uhd_image_loader --args="type=usrp2,addr=192.168.2.201" --fw-path=~/uhd-images/uhd-images_003.010.twinrx-devel-234-g6189cea6/share/uhd/images/usrp_n200_fw.bin –fpga-path=~/uhd-images/uhd-images_003.010.twinrx-devel-234-g6189cea6/share/uhd/images/usrp_n200_r4_fpga.bin

sudo uhd_cal_rx_iq_balance --verbose --args addr=192.168.2.203 --freq_start 2420000000 --freq_stop 2480000000

sudo uhd_cal_tx_iq_balance --verbose --args addr=192.168.2.203 --freq_start 2420000000 --freq_stop 2480000000

sudo uhd_cal_tx_dc_offset --verbose --args addr=192.168.2.203 --freq_start 2420000000 --freq_stop 2480000000

~/uhd-images/uhd-images_003.010.twinrx-devel-234-g6189cea6/share/uhd/images/usrp_n200_fw.bin
~/uhd-images/uhd-images_003.010.twinrx-devel-234-g6189cea6/share/uhd/images/usrp_n200_r4_fpga.bin

sudo uhd_cal_rx_iq_balance --verbose --args addr=192.168.2.201 --freq_start 915000000 --freq_stop 915000000

sudo uhd_cal_tx_iq_balance --verbose --args addr=192.168.2.201 --freq_start 915000000 --freq_stop 915000000

sudo uhd_cal_tx_dc_offset --verbose --args addr=192.168.2.201 --freq_start 915000000 --freq_stop 915000000

Khash’s PRN code
PAPR I = 2.6
PAPR Q = 2.7

0dBm is the ca-tx-tone.grc

note: subtract error to get actual gain

table
usrp_gain	error	psd_db	SNR	FS
0	-17	-146	0
5	-146	4
10	-145
15	-145
20	-144
25	-141
30	-137